## Slide 1: Cilium SRv6 Lab: A Pathway to Cloud Native SP Network Services
Bruce McDougall
Nicolas Michel
Nov 2024
Notes: Instructions:
FOR NEW SLIDES, USE “BLUE THEME 2015 16x9” MASTER SLIDES – Click New Slide button on toolbar (Home menu). Right click any slide thumbnail at far left to access available slide layouts)
Insert presentation details - speaker, title, date and architecture or solution
Before building your presentation, identify what your key topics will be, along with:
  The value it brings to the customer
  b) The technical aspect the SEs need to understand
  c) Any cautions or restrictions
  d) The relevant points for each topic SEs need to be clear on
  e) How this process or feature is different from previous iterations, if appropriate
  f) In your narration, always explain WHY the information is important AND bridge one topic to the next to demonstrate how it all fits together

## Slide 2
Intro: Cilium and eBPF (15 min)
Lab 1 – dCloud, Containerlab, XRd, Ansible (10 min)
Lab 2 – K8s Fundamentals, Deploy K8s Cluster (15 min)
Lab 3 – Cilium SRv6 L3VPN (15 min)
Lab 4 – ISIS Redistribution into the Core (10 min)
Conclusion: eBPF on Everything – IoeBPFT (15 min)

## Slide 3: The Most Important Place in the Network
Someone Else’s Network
Cisco’s Network
NIC
ToR, PE,
etc.
Servers hosting applications/workloads
Apps
Apps
Apps
Cisco’s historical Air-Gap

## Slide 4: Isovalent Closes the Host Networking Gap
With Isovalent Cisco can now:
Own the DC Fabric
Own the Virtualized/Containerized Host Stack
Own the Network Policy, Security, and Visibility Framework…E2E
Own the Conversation with NetEng, NetSec, DevOps/SRE, and Application Owners and Developers

## Slide 5: Some Logos
https://cilium.io/adopters/

## Slide 6: CNI – K8s Container Network Interface
Decoupling of Control (Cilium) and Forwarding Planes (eBPF)
Programmatic interfaces
Workload Dataplane: routing, segmentation/overlays, access control, FW, LB, NAT
Direct Mode
Overlay / Tunnel Mode
(VXLAN, Geneve, SRv6*)
Host running containers

## Slide 7
eBPF is a revolutionary technology that can run sandboxed programs in a privileged context such as the OS kernel. It is used to safely and efficiently extend the capabilities of the kernel without requiring to change kernel source code or load kernel modules.
Has its roots in Software Defined Networking

## Slide 8
Cilium Enterprise:
One Solution For Your Cloud Native Journey

## Slide 9
Intro: Cilium and eBPF
Lab 1 – dCloud, Containerlab, XRd, Ansible
Lab 2 – K8s Fundamentals, Deploy K8s Cluster
Lab 3 – Cilium SRv6 L3VPN
Lab 4 – ISIS Redistribution into the Core
Conclusion: eBPF on Everything – IoeBPFT

## Slide 10: dCloud Lab Topology
Ubuntu 22.04 VM: topology-host
32 vCPU, 96GB memory
Access dCloud via AnyConnect VPN
Containerlab
Docker
XRd image(s)
Nested Virtualization: KVM
Prebuilt nested VM images
Build your own?
  https://tbv3-ui.ciscodcloud.com/
https://wwwin-github.cisco.com/brmcdoug/cilium-srv6

## Slide 11: Containerlab
Open-source but heavily used (and maintained) by Nokia’s PLM and TMEs
Not just another GNS3, PacketTracer, Eve-NG (UnetLab for OGs), CML (VIRL), Boson NetSim (Real OGs)
  Why do we need it ? Do we want to re-invent the wheel again. ?
Containerlab is a CLI (YAML) based container orchestrator that will create your networking labs and topology, and everything needed:
  Topology Images (docker images)
  Topology Link (docker networking !)
  Support Container based Network Operating System (cNOS):
    Cisco XRd
    Sonic
    Cumulus CX
    Arista cEOS
  Support Virtual Machine based Network Operating System (vNOS):
    Cisco IOS XRv9k – Nexus 9kv – Cisco C8000v – Cisco C9000v
    Juniper vMX …
    Palo Alto PAN
    Checkpoint
    Fortinet
Perfect to learn Docker networking
Perfect to learn Linux and Linux networking
Perfect to learn YAML – JSON
Perfect to learn open source (contribute?)
Perfect to learn Isovalent/Cilium
Perfect to know how your competition software/Hardware behave (keep your friends close, keep your competition closer)
Perfect to Learn CI/CD – DevOPS (K8s) – Infrastructure as code
Perfect to learn Wireshark

## Slide 12: Alternate Lab Guide Once Connected to VPN

## Slide 13: Virtual Network Topology
Topology designed to accommodate expansion and more use cases in the future
BGP Sessions:
Today’s Lab will focus here

## Slide 14
Intro: Cilium and eBPF
Lab 1 – dCloud, Containerlab, XRd, Ansible
Lab 2 – K8s Fundamentals, Deploy K8s Cluster
Lab 3 – Cilium SRv6 L3VPN
Lab 4 – ISIS Redistribution into the Core
Conclusion: eBPF on Everything – IoeBPFT

## Slide 15: Kubernetes in One Two Slides!
https://kubernetes.io/

## Slide 16: Kubernetes in One Two Slides!
https://kubernetes.io/docs/concepts/overview/components/

## Slide 17: Two Node Kubernetes Cluster
We’ll use Kubeadm to initialize K8s Control Plane Node and Worker Node on our two nested VMs

## Slide 18
Intro: Cilium and eBPF
Lab 1 – dCloud, Containerlab, XRd, Ansible
Lab 2 – K8s Fundamentals, Deploy K8s Cluster
Lab 3 – Cilium SRv6 L3VPN
    BGP Peering
    SRv6 SID-Manager; Locator Pool
    Pods in VRFs
    SRv6 Responder
Lab 4 – ISIS Redistribution into the Core
Conclusion: eBPF on Everything – IoeBPFT

## Slide 19: Cilium/eBPF and SRv6
Bell Canada driving development
Working with AWS and GCP
Cloud-Native SRv6-L3VPN Attachment via Cilium CNI
Just the tip of the iceberg…
Dan Bernier presented at Kubecon EU 2024
https://www.youtube.com/watch?v=vJaOKGWiyvU&t=24s

## Slide 20: More Cilium SRv6 L3VPN
https://wwwin-github.cisco.com/emear-telcocloud/iblog
Arkadiusz Kaliwoda

## Slide 21: Cilium SRv6 CRDs
BGP CRD
  IPv4, IPv6, and “mpls_vpn” AFI/SAFIs
SRv6 SID Manager
  Dynamic allocation of /48 or /64 locator from LocatorPool
K8s VRFs
  Pods in VRF Blue and VRF Red
SRv6 Responder
  SRv6 EgressPolicy programing for eBPF
  Essentially the SRv6-L3VPN FIB entries
R14
R15
BGP 65010
K8s-cp-node00
ASN 65015
SRv6 Locator fc00:0:abc::/48
K8s-wkr-node01
ASN 65014
SRv6 Locator fc00:0:xyz::/48
Rest of the Network
Kubernetes Custom Resource Definions

## Slide 22
Intro: Cilium and eBPF
Lab 1 – dCloud, Containerlab, XRd, Ansible
Lab 2 – K8s Fundamentals, Deploy K8s Cluster
Lab 3 – Cilium SRv6 L3VPN
Lab 4 – ISIS Redistribution into the Core
Conclusion: eBPF on Everything – IoeBPFT

## Slide 23: Redistribute Cilium Locators into DC ISIS
Topology designed to accommodate future expansion and use cases
BGP Session:
Redistribute Locator /48s into ISIS

## Slide 24
Intro: Cilium and eBPF
Lab 1 – dCloud, Containerlab, XRd, Ansible
Lab 2 – K8s Fundamentals, Deploy K8s Cluster
Lab 3 – Cilium SRv6 L3VPN
Lab 4 – ISIS Redistribution into the Core
Conclusion: eBPF on Everything – IoeBPFT

## Slide 25: Cisco’s Air-Gap Network
Cisco’s Network
NIC
Servers hosting applications/workloads
App

## Slide 26: eBPF on Everything!
Policy Execution Data Plane Elements
Transport network
Universal policy execution engine and visibility agent for everything…in the galaxy
SP last mile, metro, or enterprise transport network
Policy Programming
Public Cloud
Policy Plane Control Elements
See also: https://isovalent.com/blog/post/networking-and-ebpf-predictions-for-2024/

## Slide 27: Cilium: A Universal SDN Policy Engine
Cilium + eBPF as a Universal SDN for Controlling and Executing Network Policy:
Security (all the firewalling, including L7 FW)
Load Balancing, Proxying, http/https/TLS ingress (no more F5)
Egress GW for cluster segments (VPC-style network gateways)
Service Mesh
BGP, SRv6, and SRv6-TE and Service Chaining…Someday
Encryption
TCP Optimization
Other workload traffic policy like QOS
And it “will be Applicable outside K8s, a distributed dataplane for the broader industry”
Distributed Policy Execution
Data Planes
Policy Control Plane

## Slide 28: https://cilium.io/labs/

## Slide 29: Resources, Links
Cilium get started
https://cilium.io/get-started/
eBPF
https://ebpf.io/
eBPF Documentary
https://www.youtube.com/watch?v=Wb_vD3XZYOA
Cilium/K8s networking eBook
https://isovalent.com/blog/post/introducing-the-new-kubernetes-networking-and-cilium-for-the-network-engineer-ebook/
Isovalent Labs
https://isovalent.com/resource-library/labs/
Swag!
https://cilium.myspreadshop.com/all
Source for this lab
https://wwwin-github.cisco.com/brmcdoug/cilium-srv6
A whole load of reference SRv6 labs
https://github.com/segmentrouting/srv6-labs

## Slide 30: Thank you